Heat and Geotherm

- In the 1800’s it was recognised that temperatures in mines and caves increased with depth. Listed below are some measurements taken in a rather deep mine. Assume steady-state equilibrium and:

  - Plot the temperature versus depth using an excel spreadsheet.

  - Either by hand or using excel’s linear trend line, draw the best fit straight line through your points and determine the thermal gradient from the slope.

  - Determine the average thermal conductivity from the values given.

  - Use the results from (b) and (c) to determine the heat flux through the surface in this region.

Depth 			Temperature 			Conductivity

km 			      °C 				Watts/(m-°C)

0.0 			11.0 				2.41

0.5 			23.0 				2.45

1.0 			36.0 				2.43

1.5 			48.0 				2.52

2.0 			61.5 				2.49

2.5 			74.0 				2.47

3.0 			85.5 				2.60

3.5 			99.0 				2.55

4.0 			110.0 				2.58

2. The relation of temperature with depth, T(y) inside the Earth may be given by:

Where Ts is the surface temperature, qs is the surface heat flux, k is the thermal conductivity, ρ is the density of the rock and H is the heat generated from radioactive decay.

- If qs 70mW/m2 , 3 g/cm3, H 1010 W/kg, k 4 Watts/(m °C) and Ts 10°C, determine the temperature profile of the upper 200 km within the Earth. Plot these points on the following page.

- Also shown on the graph paper are the liquidus (the line separating the liquid phase (or magma) of a rock from the partially molten phase) and the solidus (the line separating the solid phase of the rock from the partially molten phase), for a peridotite.

    - Determine the depth where the mantle starts to melt.

    - Does this depth correspond with any other observational attribute of the mantle?

    - At what depth is the mantle entirely liquid?

    - What observations tell us that the mantle at this depth does not heat up to such temperatures?

    - How is such melting prevented by the mantle?

- Using the parameters listed in (b), find the temperature in the crust at 5, 10, and 15 km by varying your assumption about the heat generation in crustal rocks: i) assume H = 0; no heat is generated in the rock. ii) assume H =109 watts/kg.

3. Determine the Rayleigh number for the mantle using the following physical parameters:

2 105 °C1,

g 10 m/s2,

3. 5 103 kg/m3,

106 m2/s,

1021 Pas,

ΔT = 3000oC.

Under what conditions would you expect the solid rock in the mantle to convect?

How does the convection differ for Ra>RaCr and Ra>>RaCr?