CONTROLLING HOUSE DUST MITES BY ENVIRONMENTAL MEANS

- SUMMARY FINDINGS -

Research project carried out in April 2000 - June 2002

by

University College London, University of Cambridge and South Bank University, in collaboration with Insect Research and Development Ltd.

House dust mites require a particular combination of temperature and relative humidity (RH) to flourish; in other words they are very sensitive to hygrothermal conditions. The possibility of controlling them by modifying the hygrothermal environment within the home has been recognised for some time, but investigating this approach has until now been hampered both by technical difficulties and by the need for cross disciplinary collaboration.

Responding to the challenge, a team of building scientists and acarologists has just completed a two year research project funded by the Engineering and Physical Sciences Research Council. This project has developed a sophisticated combined hygrothermal and population model of house dust mites in beds. It is the first model in the world that is capable of modelling a) the 3D hygrothermal environment within any bed, in any climate, in any dwelling and with any occupant use pattern, and b) the impact that this environment has on every stage of mite development, taking account of mite movement within the bed. Although more work is required to validate the model and to extend its applicability, the team has begun to use it to investigate which feasible modifications to home environments have most impact on mite populations. In this way it will be possible to establish the most effective, energy efficient and socially acceptable ways of achieving mite control, thereby reducing the prevalence of mite related disease.

Specific key advances in knowledge resulting from the project are as follows:

Beds          	Hygrothermal conditions in a bed are critically dependent on bedroom conditions. This is in part because beds are unoccupied and in equilibrium with room conditions for most of the time and also because, even when occupied, conditions in large areas of a bed remain similar to the room. The levels of building insulation, ventilation and heating thus have more effect than the type of bed or bedding.

·	Counter to common belief, the RH directly underneath the occupant typically decreases when a bed is occupied, although it rises in other parts of the bed. There are thus considerable spatial variations in hygrothermal conditions within the bed, as well as variations over time. Since both temperature and RH affect mite development, this highlights the importance of examining both variables.

·	Sprung mattresses result in less moisture in the bed compared to polyurethane foam mattresses. This is contrary to much current advertisement literature.

·	There are significant differences between people in terms of the moisture they generate in a bed; these differences do not appear to correlate with age, sex, or size.

Mites           	Laboratory carrying capacity experiments indicate a maximum capacity of 12,000 mites per gram of dust. Simple calculations indicate that a mattress may theoretically be able to sustain up to 1.5 million mites if both food supply and hygrothermal conditions are continuously favourable.

·	Mites do move to find more favourable hygrothermal conditions. This is important since the most favourable hygrotheral locations within a bed shift over time.

·	For the first time, Population Equilibrium Conditions have been determined, ie. the combinations of RH and temperature at which population growth is in equilibrium, neither growing nor declining.

Modelling  	Small reductions in ventilation rate below 0.5 air changes per hour can have a dramatic impact. Reducing from 0.5 to 0.4 ach will increase the mite population by 100 times. However, raising it to above 0.7 ach can lead to an increase in the mite population in a fuel poor dwelling (one where the occupants cannot heat it properly), compared with a decrease in a fuel rich dwelling.

·	Raising bedroom temperatures from 16ºC to 18ºC, ie. without reducing ventilation, will result in a ten times reduction in mite numbers. The increase in bedroom temperatures over the last 50 years, partly as a result of increased central heating and improved insulation, is therefore likely to have had beneficial effects. This supports the case for continuing to improve the nation’s housing stock.

·	Building occupant density is a key parameter in determining house dust mite populations. Increasing the number of occupants in a dwelling from 4 to 6 can increase the mite population by 10,000 due to the increased moisture production in the property.

·	Model predictions indicate that the highest mite populations should occur in the South West of England, followed by Northern Ireland, with London having the lowest. An identical property and occupant is predicted to have 400 times the mite population in SW England compared to London. Such regional differences in mite populations may in part explain regional differences in asthma.

·	Climate change is likely to result in a significant increase in mite populations. For example (using the 1998 UK Climate Impacts Programme climate predictions) a typical bed in London is predicted to have 80 times the population of mites in 2050.

More detailed information

A follow-up project is currently being undertaken.

Contacts: Prof Tadj Oreszczyn (UCL) t.oreszczyn@ucl.ac.uk 020 7504 5906; Dr David Crowther (UC) drgc2@cam.ac.uk 01223 331700